## Slide 1: Missouri River Basin Water Management Mid-West power users association
John Remus
Chief, Missouri River Basin Water
Management Division
December 12, 2019
Denver, Colorado

## Slide 2: Outline/house keeping
  Summarize 2019
  2020 Outlook
  House Keeping (Litigation)
    There are a number of ongoing legal actions in the basin.
    I will not be answering questions or commenting on any ongoing litigation.
    The court’s opinions/decisions are not final, and as such, commenting on any ongoing litigation is against Corps policy.
    The Corps will continue to meet our statutory obligations to operate the Missouri River Mainstem System for its authorized purposes.

## Slide 3: MISSOURI RIVER MAINSTEM RESERVOIR SYSTEM

## Slide 4: Missouri river mainstem reservoir system
FORT PECK
GARRISON
BIG BEND
GAVINS POINT
OAHE
FORT RANDALL

## Slide 5: Our mission Regulate Missouri River Mainstem Reservoirs
  Priority: Life and Safety
  Operational Decisions: Driven by Annual Runoff Conditions
  Water captured in System flood control storage zones each year must be evacuated prior to the start of the following year’s runoff season.
  Master Manual: Storage and release decisions designed significantly around Flood Control, Navigation & Water Supply purposes
  Authorized Purposes:
  Authorized Purposes:
Flood Control | Navigation | Hydropower | Water Supply | Fish & Wildlife | Irrigation | Water Quality Control | Recreation
HYDROPOWER
NAVIGATION
FLOOD CONTROL
WATER SUPPLY
RECREATION
IRRIGATION
WATER QUALITY CONTROL
FISH & WILDLIFE
Federal Laws: The Corps complies with all federal laws.

## Slide 6: Mainstem Reservoir Storage Capacity

## Slide 7: Missouri River Mainstem System Storage Zones and Allocations
17.6
56.1
67.7
72.4
EXCLUSIVE FLOOD CONTROL 7%
PERMANENT
POOL 24%
ANNUAL FLOOD CONTROL &
MULTIPLE USE 16%
CARRYOVER MULTIPLE
USE 53%
0
STORAGE IN MILLION ACRE FEET (MAF)
Historic max - 2011
Historic min – 2007
72.8
33.9
WE ARE HERE
DEC 3, 2019 – 57.4

## Slide 8: 2019 summary

## Slide 9: NATIONAL WEATHER SERVICE
Rain-on-Snow Event of March 12th-14th 2019
Rain-Snow line
Notes: NOHRSC SWE as of 11 March, overlaid by rain-on-snow event starting roughly midnight of 12th-13th, and concluding early on 14th. Add to that deeply frozen ground with perhaps an 85% runoff to precip/melt ratio. That’s a guess as to ratio.
Basically, you had widespread 2 inch rain over widespread 2-4 SWE. So a 2 inch rainstorm becomes a 5-inch rainstorm (and with frozen ground and no infiltration, it may be like a 7-8 inch rainstorm).

## Slide 10: NATIONAL WEATHER SERVICE
Mid-March 2019 Event
Notes: Set over 40 new records (provisional, not officially declared yet)

## Slide 11: ESTIMATED PEAK FLOWS
Mid-March 2019 Event
Notes: Set over 40 new records (provisional, not officially declared yet)

## Slide 12: precipitation
Source: NOAA National Centers for Environmental Information

## Slide 13: Monthly Runoff above Sioux City, IA
Chart: 2019 CALENDAR YEAR FORECAST – 60.4 MAF
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
2019 Forecast | 850 | 1150 | 10958 | 7765 | 8899 | 8707 | 6985 | 3340 | 4910 | 3186 | 2037 | 1607
Average | 775 | 1123 | 2923 | 2919 | 3337 | 5473 | 3278 | 1365 | 1148 | 1202 | 1046 | 761
Observed
Average
Forecast

## Slide 14: Annual Runoff above Sioux City, IA
Chart: YEARS
Drought Periods | 18452 | 10600 | 19500 | 18220 | 11060 | 14320 | 14060 | 14634 | 20636 | 17038 | 12024 | 16675 | 19149 | 16329 | 19454 | 21972 | 16973 | 19899 | 20332 | 12507 | 21254 | 12352 | 17700 | 16691 | 22330 | 16448 | 16678 | 22537 | 16002 | 17594 | 16162 | 20077 | 18300 | 20300 | 0
Current Forecast | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
2019 Forecast
Historic Drought Periods
Median
U.D.
U.Q.
L.D.
L.Q.

## Slide 15: Fall / Winter Releases
  Gavins Point Dam releases will be reduced to winter rate by mid-December (includes 10-day extension)
  Corps will closely monitor channel/ice conditions between reservoirs and downstream of Gavins Point Dam
  Above-average winter releases needed to complete evacuation of stored flood waters
  Expected releases (in 1000 cfs):
 |  | Dec | Jan | Feb | 
Fort Peck |  | 13.0 | 13.0 | 13.0 | 
Garrison Oahe |  | 21.3 33.8 | 24.5 27.4 | 24.5 26.3 | 
Gavins Point |  | 32.6 | 25.0 | 25.0 | 

## Slide 16: Hydropower production

## Slide 17: 202o OUtlook

## Slide 18: Drought Conditions and soil moisture
Source: National Drought Mitigation Center
Source: NWS Climate Prediction Center
No drought conditions in the Missouri River Basin.
VERY wet soil conditions, particularly in the upper Missouri River Basin.

## Slide 19: Temperature and Precipitation Outlooks
Source: NWS Climate Prediction Center
Temperature
Dec-Jan-Feb
Precipitation
Increased chances for wetter-than-average precipitation in most of the upper Basin.
Equal chances for warmer-average-colder temperatures in most of the Basin.

## Slide 20: snowpack
Source: National Hydrologic Remote Sensing Center Center
Plains Snowpack (Dec 3)
Mountain Snowpack
Source: USDA, Natural Resources Conservation Service

## Slide 21: System Storage - 2019-2020 Draft AOP
Chart: YEARS
Top of Exclusive Flood Control – 72.4 MAF
Base of Exclusive Flood Control – 67.7 MAF
Base of Annual Flood Control – 56.1 MAF
2019
2020
2021
System Storage Check
Upper Decile and Lower Decile
Median

## Slide 22
Mainstem Reservoir Status:
System storage is 57.4 MAF; 1.3 MAF of the 16.3 MAF of flood control storage is occupied, and will be evacuated before the start of the 2020 runoff season.
A snowstorm over the weekend led to accumulated plains snowpack over much of the upper basin (upper right graphic). Mountain snowpack is also accumulating at near average rates (click here).
Gavins Point releases are currently 70,000 cfs, and will be reduced to 65,000 cfs today, and further reduced by 3,000 cfs every day until the release rate of 27,000 cfs is reached. Releases may be reduced to 25,000 cfs in January. The drawdown schedule is shown in the bottom right quadrant. Basin and river conditions will continue to be monitored, and System regulation will be adjusted as necessary.
The 2019 calendar year runoff forecast above Sioux City, updated on December 2, is 60.4 MAF (238% of average).
Refer to the 3-Week Forecast (click here) for the most up-to-date System information – pool levels, inflows and releases.
The Gavins Point release schedule and forecasted Missouri River flows and stages can be found here:
http://www.nwd-mr.usace.army.mil/rcc/reports/pdfs/weeklyupdate.pdf
Missouri River Basin – Update – 3 December 2019
Click Here for Latest 3-Week Forecast
Click Here for Comparison Plots
2250
2246
2234
2160
2030
Elevation in feet msl
Current Reservoir Levels
Elevation in feet msl
Storage in MAF
Fort Peck
Garrison
Oahe
System Storage
1850
1837.5
1775
1673
1854
Elevation in feet msl
1617
1607.5
1540
1415
67.7
56.1
17.6
0
1620
72.4
Exclusive Flood Control
Exclusive Flood Control
Exclusive Flood Control
Exclusive Flood Control
Annual Flood Control & Multiple Use
Annual Flood Control & Multiple Use
Annual Flood Control & Multiple Use
Annual Flood Control & Multiple Use
Carryover Multiple Use
Carryover Multiple Use
Carryover Multiple Use
Carryover Multiple Use
Permanent Pool
Permanent Pool
Permanent Pool
Permanent Pool
Current Storage
57.4
1839.0
2238.6
1609.1
4.6 feet above the base of flood control.
1.5 feet above the base of flood control.
1.6 feet above the base of flood control.
1.3 MAF above the base of flood control.
Click Here for Missouri River releases, flows & stages
*Source: https://www.nohrsc.noaa.gov
Gavins Point Release Reduction Schedule
Plains Snowpack
December 1, 2019

## Slide 23: Thank You!
John Remus, P.E. | john.i.remus@usace.army.mil | 402.996.3840
Kevin Grode, P.E. | kevin.r.grode@usace.army.mil | 402.996.3870
Mike Swenson, P.E. | michael.a.swenson@usace.army.mil | 402.996.3860
Email: | Missouri.Water.Management@usace.army.mil | 
Website: | www.nwd-mr.usace.army.mil/rcc/ nwd.usace.army.mil/MRWM | 
Search: | Corps Missouri River on Google | 
Social Media: | Facebook: nwdusace #MissouriRiver Twitter: nwdusace #MORiver #MissouriRiver |